## Slide 1: Extra-Tropical Storm Surge (ETSS) Model and Post Processing V 2.0
Pre-Implementation Briefing
December, 2014
Huiqing Liu, Ryan Schuster, and Arthur Taylor
MDL/NWS/NOAA

## Slide 2: Outline
Project Description
  What is ETSS?, What is SHEF?, Why are we doing this?
Quad Chart
  Scope and benefits
ETSS 2.0 Flow Chart
Testing
Resources
Dissemination
Repository
Architecture

## Slide 3: What is ETSS?
The Extra Tropical Storm Surge Model is a modification of the SLOSH model which uses GFS winds to predict storm surge based on large extra-tropical storms
Produces Coastal Guidance
  4 times a day (00z, 06z, 12z and 18z) when the GFS winds are available (roughly 4 hours 50 min after nominal forecast time)
  On NDFD CONUS Grid (merges 3 extra-tropical basins)
  On NDFD Alaska Grid (merges 3 extra-tropical basins)

## Slide 4: What is SHEF?
  Standard Hydrometeorological Exchange Format
  Designed for data sharing and readability
    Identifies location, data type, time and interval of measurements, units
  Example:
  ****0000021076****CBOFS KWBC 061842
  TIDNT
  :SHEF ENCODED 30 MINUTE WATER LEVEL FORECAST GUIDANCE
  :WATER LEVEL VALUES REFERENCED TO MLLW IN FEET (HMIFZ)
  :TIME ZONE IS UTC
  :WATER LEVEL FORECAST GUIDANCE IS FOR TOTAL WATER LEVELS
  :PROVIDED BY DOC/NOAA/NOS/CO-OPS
  :corms@noaa.gov 301-713-2540
  .E SWPV2 20120906 Z DH1200/HMIFZ/DIN30/ 0.427 / 0.887 / 1.122 / 1.435 / 1.646 / 1.865
  .E1 2.065/ 2.219 / 2.446 / 2.589 / 2.676 / 2.767 / 2.665 / 2.500 / 2.322 / 2.156 / 1.939 / 1.764
  .E2 1.602/ 1.407 / 1.251 / 1.057 / 0.925 / 0.789 / 0.781 / 0.880 / 1.045 / 1.230 / 1.414 / 1.616
  .E3 1.820/ 2.007 / 2.182 / 2.363 / 2.453 / 2.538 / 2.498 / 2.405 / 2.288 / 2.128 / 1.994 / 1.820
  .E4 1.631/ 1.385 / 1.184 / 1.027 / 0.931 / 0.897 / 0.943 / 1.046 / 1.175 / 1.347 / 1.563 / 1.812
  .E5 2.087/ 2.375 / 2.632 / 2.855 / 3.002 / 3.111 / 3.150 / 3.104 / 3.001 / 2.853 / 2.699 / 2.524
  .E6 2.322/ 2.086 / 1.812 / 1.537 / 1.313 / 1.164 / 1.073 / 1.065 / 1.116 / 1.191 / 1.267 / 1.352
  .E7 1.464/ 1.598 / 1.754 / 1.916 / 2.050 / 2.139 / 2.167 / 2.138 / 2.071 / 1.972 / 1.848 / 1.715
  .E8 1.573/ 1.419 / 1.239 / 1.042 / 0.866 / 0.724 / 0.648

## Slide 5: Why are We Doing This?
“Depending on the storm event, in the upper reaches of some tidal rivers, flooding from storm surge may be followed by river flooding from rain in the upland watershed. This increases the flood severity.” – NOAAWatch.gov
River forecast centers (RFCs) use AHPS and lack system-friendly predictions at the coastal interface (i.e. river mouths)
Bias-corrected SHEF output from ETSS would provide that guidance in an AHPS-readable format
Data also available on AWIPS for WFOs

## Slide 6
6
Extra Tropical Storm Surge V2.0
Project Status as of 11/3/2014
Issues/Risks
Finances
Scheduling
Project Information and Highlights
Lead: Huiqing Liu, Ryan Schuster, Arthur Taylor, MDL and Becky Cosgrove, NCO
Scope:
Nesting coarse extra-tropical grid and existing fine scale tropical basins – for East Coast and Gulf of Mexico
This Implementation will add over land calculations
Will also add tidal forcing.
Operationalize ETSS post processing by porting the code the computes total water level guidance to an NCO approved programming language
Provide NCO with code to SHEF encode the total water level guidance
Expected Benefits:
Computes inundation based on (a) surge, and (b) latest overland grids from the tropical program.
Provide RFC’s via AHPS surge plus tide bias corrected guidance
Make post processing of extra tropical storm surge more robust
Associated Costs: Federal FTE labor and Contract Support
Funding Sources: MDL Base and Sandy Supplemental
Computational Resources:
Currently – 2 CPU for 5 minutes
Will use – 6 CPU for 35 minutes (Model) + 3 CPU for 8 minutes (Post Processing).
Management Attention Required
G
R
v1.0 09/14//07
Y
G
Issues:
-- Adding point data to SBN (needs headers)
-- Determine which variables / stations to SHEF encode
Risks:
-- Headers are not available
-- Don’t determine the right variables / stations
Mitigation:
-- Coordinate with data management / TOC
-- Coordinate with AHIPS / RFC contacts
Milestone (NCEP) | Date | Status
Initial coordination with SPA team | 12/16/2014 | 
MDL testing complete | 1/16/2015 | 
Final Code Delivered to NCO | 1/16/2015 | 
Technical Information Notice Issued | 2/1/2015 | 
SPA begins prep work for 30 day test | 1/19/2015 | 
30-day evaluation begins | 2/16/2015 | 
30-day evaluation ends | 3/17/2015 | 
IT testing ends | 2/13/2015 | 
Management Briefing | 3/27/2015 | 
Operational Implementation | 3/31/2015 | 
Y
R
6
Potential Management Attention Needed
On Track
R
G
G
G

## Slide 7
Project Scope and Benefits
Scope:
Nest coarse and fine scale model basins
Introduce overland flooding calculations
Produce SHEF-encoded bias-corrected total water level guidance at coastal stations
Provide SHEF messages to river forecast centers (RFCs)
Benefits:
Computes inundation based on surge, and latest overland grids from the tropical program.
ETSS post-processing becomes more robust and reliable
RFCs receive hourly guidance within their forecast system

## Slide 8
runETSS.sh
Prepare to define GFS data source and Model working directory
Kick off setup.sh and check.sh to copy GFS data needed by ETSS. Also kick off jgfs_stormsurge.ecf
Kick off Cron Job at
04:50z, 10:50z, 16:40z ,22:40z ,
for GFS output data time delay
Submit job JGFS_STORMSURGE
Kick off script exgfs_stormsurge_sh.ecf
Prepare GFS data and run mdl_c10_gen mdl_cy_puv10
gfs_stormsurge*poe.sh run
ETSS2.0
Run mdl_mdlsurge
mdl_gridmerge
Output Data and kick off post-processing
Pre processing GFS wind data
mdl_c10_gen extract past forcing fields
mdl_cy_puv10 extract current and forecast forcing fields
Assign 6 cpu to first run ETSS 2.0 model in 6 extra tropical basins and then assign 6 cpu to run in tropical basins
Post processing output data
mdl_mdlsurge handle stations output
mdl_gridmerge handle whole grid output
Stations output files are in text format
whole grid output files are in GRIB-2 format
ETSS 2.0 running at 00z, 06z, 12z and 18z

## Slide 9
Post.ETSurge2.0 running for 00z, 06z, 12z and 18z
runMe.sh
defines working directory and calls kickoff job
JETSURGE_KICKOFF sets up env vars and starts exetsurge_kickoff.sh.ecf
Kicked off after ETSS2.0 model run
exetsurge_kickoff.sh.ecf gets surge and BUFR obs data, kicks off ECFs:
jetsurge_parsedat.ecf runs JETSURGE_PARSEDAT
jetsurge_griddat.ecf waits for JETSURGE_PARSEDAT then runs JETSURGE_GRIDDAT
jetsurge_combdat.ecf waits for JETSURGE_GRIDDAT then runs JETSURGE_COMBDAT
Output SHEF
Runs exetsurge_parsedat.sh.ecf to debufr obs
Runs exetsurge_griddat.sh.ecf to predict tide and grid surge, tide, and obs
Runs exetsurge_combdat.sh.ecf to calculate anomaly, compute bias-corrected total water level and SHEF-encode the result

## Slide 10: Testing
Model
Ran from Oct. 24, 2014 to now
  Compared to ETSS1.5: http://nws.weather.gov/mdl/surge/comparison/comp1/
Post - Processing
SHEF-encoded output successfully tested using AHPS system to decode
  AHPS contact: Mark Armstrong (mark.armstrong@noaa.gov)
Ran on WCOSS Dev machine for several weeks with correct output and format
  Compared to ETSS1.5 text product and plots: http://www.nws.noaa.gov/mdl/etsurge
Eval Team (Proposed)
NCO, MDL, OPC, NHC/TAFB, WFOs coordinated via OCWWS
AHPS contact could test SHEF-output for 30-day period

## Slide 11: Resources
CPU
  Model: 6 CPU for 35 minutes
  Post-Processing: 3 CPU for 8 minutes
Output files:
  Model: 55 MB CONUS grids and 125 MB ALASKA grids 4x per day (720 MB per day total)
  ASCII SHEF bulletins: 226KB , 4x per day (904 KB per day total)
  CSVs for site are 34MB (put tar.gz size instead)

## Slide 12: Dissemination
Model output into /com and /pcom
NWS FTP: http://weather.noaa.gov/pub/SL.us008001/DF.anf/DC.etss/
SHEF-encoded output:
WMO headers
  CONUS: SRUS70 KWNO
  Alaska: SRAK70 KWNO
AWIPS IDs
  East coast: TIDTWE, Gulf of Mexico: TIDTWG, West Coast: TIDTWP, Gulf of Alaska: TIDTWC, Bering Sea: TIDTWB, Arctic Alaska: TIDTWA
DBNet Alert
  Dbn_alert: YYYY-mm-ddTHH:MM:SS MDLFCST ETSSBULL ${job} ${pcom}/${our_dir}/etss.tCCz.bull_tar

## Slide 13: Repository
SVNs: https://vlab.ncep.noaa.gov/svn/etss/gfs_stormsurge/trunk https://vlab.ncep.noaa.gov/svn/etss/post.etsurge2.0/trunk
Project Pages: https://vlab.ncep.noaa.gov/redmine/projects/etss/repository/show/gfs_stormsurge https://vlab.ncep.noaa.gov/redmine/projects/etss/repository/show/post.etsurge2.0

## Slide 14: Questions for the SPA

## Slide 15: Architecture ETSS1.5
Data Source: /com/gfs/prod/gfs.${PDY}
Data Destination: ${MDLTEST_DIR}/com/gfs/prod/gfs.${PDY}
Model Working Directory: ${MDLTEST_DIR}/tmp
MDLTEST_DIR: ~/etss1.5/work
Step 0: “runETSS.sh YYYYMMDD XX”
a) Copy GFS input data from /com to ${MDLTEST_DIR}/com
b) Copy ETSS 1.0 output data from /pcom to ${MDLTEST_DIR}/pcom
c) Call myEcf/jgfs_stormsurge.ecf to call jobs/JGFS_STORMSURGE via bsub
Step 1: jobs/JGFS_STORMSURGE
a) Set environment variables and call ‘mpirun.lsf scripts/exgfs_stormsurge.sh.ecf’
Step 2: scripts/exgfs_stormsurge.sh.ecf “prepare GFS data step”
a) Prepare GRIB-2 0.5 degree resolution data before running extraction programs
b) Run mdl_c10_gen to extract past (60 hours)surface pressure, and wind vector
fields from GRIB-2 0.5 degree data for 6 extra-tropical basins
c) Run mdl_cy_puv10 to extract current and forecast(96 hours) surface pressure,
and wind vector fields from GRIB-2 0.5 degree data for 6 extra-tropical basins

## Slide 16: Architecture ETSS2.0
Data Source: /com/gfs/prod/gfs.${PDY}
Data Destination: ${MDLTEST_DIR}/com/gfs/prod/gfs.${PDY}
Model Working Directory: ${MDLTEST_DIR}/tmp
MDLTEST_DIR: ~/etss2.0/dev/work
Step 0: “dev/runETSS.sh YYYYMMDD XX”
a) Copy GFS input data from /com to ${MDLTEST_DIR}/com
b) Copy ETSS 1.5 output data from /pcom to ${MDLTEST_DIR}/pcom
c) Call dev/myEcf/jgfs_stormsurge.ecf to call jobs/JGFS_STORMSURGE via bsub
d) Call ../../Postetss2.0/dev/runMe.sh to kickoff post etss2.0 run
Step 1: jobs/JGFS_STORMSURGE
a) Set environment variables and call ‘mpirun.lsf scripts/exgfs_stormsurge.sh.ecf’
Step 2: scripts/exgfs_stormsurge.sh.ecf “prepare GFS data step”
a) Prepare GRIB-2 0.5 degree resolution data before running extraction programs
b) Run mdl_c10_gen to extract past (60 hours)surface pressure, and wind vector
fields from GRIB-2 0.5 degree data for 6 extra-tropical basins and 29 tropical
basins
c) Run mdl_cy_puv10 to extract current and forecast(96 hours) surface pressure,
and wind vector fields from GRIB-2 0.5 degree data for 6 extra-tropical basins
and 29 tropical basins

## Slide 17: Architecture ETSS1.5
Step 3: scripts/exgfs_stormsurge.sh.ecf “run ETSS1.5 model step”
a) Call ush/gfs_stormsurge_poe.sh assign 1 CPU to run extra-tropical storm surge
model in Gulf of Mexico basin and the other 1 CPU to run in other 5 basins.
*) Bi-linear interpolate Atmospheric forcing fields (surface pressure, and U and V
wind vector fields) from GFS 0.5 degree grids to SLOSH extra-tropical basin
grids
*) Generate surge archive files: 1)sshistory.${cyc}${bsn} (station output)
2)ssgrid.${cyc}${bsn} (whole domain)

## Slide 18: Architecture ETSS2.0
Step 3: scripts/exgfs_stormsurge.sh.ecf “run ETSS2.0 model step”
a) Call ush/gfs_stormsurge_poe.sh assign 6 CPU to run extra-tropical storm surge
model in 6 extra-tropical basins and then call ush/gfs_stormsurge_nest_poe.sh
assign 6 CPU to run extra-tropical storm surge in 29 tropical basins using nesting
boundary outputted from the previous runs in extra-tropical basins.
*) Bi-linear interpolate Atmospheric forcing fields (surface pressure, and U and V
wind vector fields) from GFS 0.5 degree grids to SLOSH extra-tropical and tropical
basin grids
*) Generate surge archive files: 1)sshistory.${cyc}${bsn} (station output)
2)ssgrid.${cyc}${bsn} (whole domain)

## Slide 19: Architecture ETSS1.5
Step 4: scripts/exgfs_stormsurge.sh.ecf “post processing output data step”
a) Run program mdl_mdlsurge to extract storm surge output at stations
sshistory.${cyc}${bsn} to AFOS format output mdlsurge.${cyc}{bsn}
b) Run program mdl_gridmerge and mdl_gridmerge_2.5km to merge grids
=> 3 Alaska area basins (ssgrid.${cyc}a,ssgrid.${cyc}z and ssgrid.${cyc}k) are
merged to GRIB-2 NDFD Alaska grids:
6 km NDFD Alaska grids mdlsurgegrid.${cyc}ala (mdl_gridmerge)
3 km NDFD Alaska grids mdlsurgegrid.3km.${cyc}ala (mdl_gridmerge_2.5km)
* need mask files: parm/mask_alaska_6km.bin (6 km resolution)
parm/mdl_etalaska.bin (3 km resolution)
=> 3 CONUS area basins (ssgrid.${cyc}e,ssgrid.${cyc}g and ssgrid.${cyc}w) are
merged to GRIB-2 NDFD CONUS grids:
5 km NDFD CONUS grids mdlsurgegrid.${cyc}con (mdl_gridmerge)
2.5 km NDFD CONUS grids mdlsurgegrid.2.5km.${cyc}con (mdl_gridmerge_2.5km)
* need mask files: parm/mask_conus_5km.bin (5 km resolution)
parm/mdl_etconus.bin (2.5 km resolution)
c) Run program tocgrib2super to add WMO super and individual headers to GRIB-2 files
* mdlsurgegrid.*${cyc}${area}===>grib2.mdlsurgegrid.*${cyc}${area}

## Slide 20: Architecture ETSS2.0
Step 4: scripts/exgfs_stormsurge.sh.ecf “post processing output data step”
a) Run program mdl_mdlsurge to extract storm surge output at stations
sshistory.${cyc}${bsn}to AFOS format output mdlsurge.${cyc}{bsn},in which
mdlsurge.${cyc}e and mdlsurge.${cyc}g use results from 2 extra-tropical basins
and 29 tropical basins
b) Run program mdl_gridmerge to merge grids
=> 3 Alaska area basins (ssgrid.${cyc}a,ssgrid.${cyc}z and ssgrid.${cyc}k) are
merged to GRIB-2 NDFD Alaska grids:
3 km NDFD Alaska grids mdlsurgegrid.3km.${cyc}ala (mdl_gridmerge_2.5km)
* need mask files: parm/mdl_etalaska.bin (3 km resolution)
=> 3 extra-tropical and 29 tropical CONUS area basins (ssgrid.${cyc}${bsn}) are
merged to GRIB-2 NDFD CONUS grids:
2.5 km NDFD CONUS grids mdlsurgegrid.2.5km.${cyc}con (mdl_gridmerge_2.5km)
* need mask files: parm/mdl_etconus_etss2.bin (2.5 km resolution)
c) Run program tocgrib2super to add WMO super and individual headers to GRIB-2 files
* mdlsurgegrid.*${cyc}${area}===>grib2.mdlsurgegrid.*${cyc}${area}

## Slide 21: Architecture Post.ETSurge2.0
Data Source: /com/gfs/prod/gfs.${PDY}
Data Destination: ${MDLTEST_DIR}/com/gfs/prod/gfs.${PDY}
Post-processing Working Directory (${DATA}): ./dev/tmp/data/tmpnwprod1/etsurge2_test.${pid}
Step 0: “runMe.sh”
a) Set up root and working directory environment variables
b) Call jobs/JETSURGE_KICKOFF
Step 1: jobs/JETSURGE_KICKOFF
a) Set more environment variables and call scripts/exetsurge_kickoff.sh
b) exetsurge_kickoff.sh copies ETSS text output and COOPS water
level obs in BUFR format from data tanks; stores in ${DATA}
c) Calls the three scripts in dev/tmp/myEcf: jetsurge_parsedat.sh.ecf,
jetsurge_griddat.sh.ecf, jetsurge_combdat.sh.ecf
Step 2: parsedat
a) dev/tmp/myEcf/jetsurge_parsedat.sh.ecf uses bsub to kick off jobs/JETSURGE_PARSEDAT
b) jobs/JETSURGE_PARSEDAT sets up some environmental vars and calls scripts/
exetsurge_parsedat.sh
c) scripts/exetsurge_parsedat.sh creates a poescript in ${DATA} to parse BUFR files (poescript_obsraw). Mpirun.lsf then runs the BUFR-parsing scripts in parallel

## Slide 22: Architecture Post.ETSurge2.0
Step 3: griddat
a) dev/myEcf/jetsurge_griddat.sh.ecf waits for myEcf/jetsurge_parsedat.sh.ecf to
finish parsing raw BUFR files then calls jobs/JETSURGE_GRIDDAT
b) jobs/JETSURGE_GRIDDAT sets up some environmental variables and then calls
scripts/exetsurge_griddat.sh to create poescript_grid in ${DATA}, which is
then run using mpirun.lsf
c) poescript_grid is a list of three commands:
- obsAll: Grids parsed BUFR obs data
- surgeAll: Parses surge text product into gridded surge data
- tideAll: Calculates tides and grids them
Step 4: combdat
a) myEcf/jetsurge_combdat.sh.ecf waits for myEcf/jetsurge_griddat.sh.ecf to
finish and then calls jobs/JETSURGE_COMBDAT
b) jobs/JETSURGE_COMBDAT sets up some environmental variables and calls
scripts/exetsurge_combdat.sh
c) scripts/exetsurge_combdat.sh simply calls the exec/combAll to calculate
anomaly and total water level from the gridded obs, surge, and tide, and
turn the results into output SHEF encoded messages for each location.